## Slide 1
MADE BY MATT / GROW TEXTILES
Make, test and improve
Autumn 1 · Week 7 · Textiles
01
Bring back your Week 6 plan. Build the pocket or agreed flat decoration.
Record what you actually make, inspect or model.
Which two checks matter most for the pocket?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Newly authored Week 7 completion from GROW Autumn SOW row 165: make/evaluate a textile item. No uploaded Week 7 textile deck was supplied; uploaded Week 5–Week 6 provide the precursor work.
Pupil prompt: Which two checks matter most for the pocket?
Teacher answer / acceptable response: The 60 × 50 mm card fits and both side joins hold through three gentle cycles.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 2
MADE BY MATT / GROW TEXTILES
Words that help
Autumn 1 · Week 7 · Textiles
02
CONSTRUCT
CRITERION
Put the planned parts together.
One check in the design brief.
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Read each word aloud and link it to a concrete example. Revisit these words during the tasks.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 3
MADE BY MATT / GROW TEXTILES
Check before making
Autumn 1 · Week 7 · Textiles
03
Adult confirms the actual material, cold tape and tool arrangements.
Check your prepared blank and fold marks against the pattern.
Know the tape’s required pressing and handling/cure time.
What if the adhesive cannot be tested before the lesson ends?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Never shorten manufacturer preparation/cure requirements to fit the timetable.
Pupil prompt: What if the adhesive cannot be tested before the lesson ends?
Teacher answer / acceptable response: Record not yet tested, let it cure and use the supplied fictional record or ready paper model for evaluation.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 4
MADE BY MATT / GROW TEXTILES
Dry-fold first
Autumn 1 · Week 7 · Textiles
04
Short edge at the top. Bottom panel folds up at 100 mm.
Top 30 mm flap folds down. Reopen the blank before adding side tape.
Check the test card has space; keep the opening clear.
Where do the two tape strips go?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Model exact fold direction with paper; an adult can position the material if agreed. This slide models the pocket. Flat-decoration makers centre the smaller panel instead of folding; use the alternative construction card.
Pupil prompt: Where do the two tape strips go?
Teacher answer / acceptable response: Along the bottom panel’s outer 10 mm side strips, from 100 mm down to 170 mm.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 5
MADE BY MATT / GROW TEXTILES
Construct from your plan
Autumn 1 · Week 7 · Textiles
05
Pocket: join the two side strips, fold up and press as directed.
Decoration: centre the small panel and join its two side strips; no folding is needed.
Add the planned symbol after checking preparation and handling times.
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Use the complete construction card. For the decoration route, follow its two-panel construction instead.
Pupil prompt: What can the checker confirm before the join is fixed?
Teacher answer / acceptable response: The side joins and edge or panel alignment match the chosen pattern. A pocket’s opening remains clear.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 6
MADE BY MATT / GROW TEXTILES
Construct from your plan — continued
Autumn 1 · Week 7 · Textiles
06
What can the checker confirm before the join is fixed?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Use the complete construction card. For the decoration route, follow its two-panel construction instead.
Pupil prompt: What can the checker confirm before the join is fixed?
Teacher answer / acceptable response: The side joins and edge or panel alignment match the chosen pattern. A pocket’s opening remains clear.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 7
MADE BY MATT / GROW TEXTILES
A controlled function check
Autumn 1 · Week 7 · Textiles
07
When ready: pocket—insert and remove the card three times; decoration—lift gently from the desk three times.
Check both side joins after each cycle and record what happened.
Keep a pocket’s opening upwards. Do not shake, swing or overload either item.
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
The test is limited to the card-pocket purpose. Flat decoration uses three gentle lifts from the desk, checking both panel joins.
Pupil prompt: What result would show the side-join check is met?
Teacher answer / acceptable response: Both joins remain attached through all three gentle checks for the chosen item. These results apply only to this limited classroom task.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 8
MADE BY MATT / GROW TEXTILES
A controlled function check — continued
Autumn 1 · Week 7 · Textiles
08
What result would show the side-join check is met?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
The test is limited to the card-pocket purpose. Flat decoration uses three gentle lifts from the desk, checking both panel joins.
Pupil prompt: What result would show the side-join check is met?
Teacher answer / acceptable response: Both joins remain attached through all three gentle checks for the chosen item. These results apply only to this limited classroom task.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 9
MADE BY MATT / GROW TEXTILES
Read a prototype record
Autumn 1 · Week 7 · Textiles
09
Sample Pocket B: correct size; card fits at first; left join opens on cycle 2.
The front stripe is clear and the approved preparation was completed.
Which criterion is not yet met?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Use the full fictional records if live handling is not possible; do not pass sample results off as a pupil’s practical evidence.
Pupil prompt: Which criterion is not yet met?
Teacher answer / acceptable response: The side join staying closed through three cycles. The record supports the other stated checks.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 10
MADE BY MATT / GROW TEXTILES
Improve one useful thing
Autumn 1 · Week 7 · Textiles
10
Name the specific issue and ask before repairing a join.
Change one thing that addresses that issue.
Repeat the relevant check when the repair is ready to handle.
Would adding a larger symbol repair an opening side join?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Keep repairs within the approved method. If time/cure is insufficient, record the next step accurately.
Pupil prompt: Would adding a larger symbol repair an opening side join?
Teacher answer / acceptable response: No. Repair or redesign the join under adult direction, then retest it.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 11
MADE BY MATT / GROW TEXTILES
Give the evidence-based verdict
Autumn 1 · Week 7 · Textiles
11
Use met, not yet or need evidence for each brief check.
Say what you made and the support you used.
Store the item safely; return tools, collect scraps and reset.
What can you truthfully record if you only made the paper model?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Assess practical process, reasoning and improvement. No personal-disclosure, touch or artistic-neatness requirement.
Pupil prompt: What can you truthfully record if you only made the paper model?
Teacher answer / acceptable response: A paper construction/fit model was made; fabric-join performance still needs evidence.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]

## Slide 12
MADE BY MATT / GROW TEXTILES
Show the design cycle
Autumn 1 · Week 7 · Textiles
12
Finish: “I checked ___; the evidence was ___; next I will ___.”
Does a neat photograph prove every check passed?
Notes: GROW_TEXTILES_W7 | Make, test and improve
Follow the plan to assemble a prototype, evaluate its function using evidence and make a targeted improvement.
Record individual response using speech, pointing, drawing or scribing.
Pupil prompt: Does a neat photograph prove every check passed?
Teacher answer / acceptable response: No. It cannot establish test cycles, cure time or the original material/tool approval.
Support: Offer premade fold marks, pre-cut strips and one visible construction step at a time. Learners may direct a maker, point to a check or use paper. Adult support is agreed; no forced physical guidance.
Stretch: Separate size, initial fit and repeated-join evidence; justify a targeted change and identify what an additional long-term test would need to investigate without claiming it has been done.
Safeguarding / safety: Follow the school practical-work risk assessment and individual access plans. The default lessons use no needles, pins, irons, hot glue, cord loops or loose buttons/beads. Adults control, count and return scissors and any small test equipment; pre-cut pieces are available. Use only school-approved cold adhesives according to the actual product instructions, check skin/material sensitivities privately, and keep glue away from eyes and mouths. Touching fabric, wearing an item or accepting physical guidance is never required. Agree support; use demonstration, pointing, an observer role or a paper/card model. Keep personal identifiers and pupil photos off public website files.
40-minute lesson flow (total for the whole lesson, not each slide):
3 min: Retrieve plan and choose role/material route.
5 min: Adult approval and model folds/joins.
17 min: Construct planned prototype or paper model.
7 min: Record function evidence and targeted improvement/retest or sample verdict.
6 min: Count and return scissors, tools and sample pieces; close approved adhesive containers, collect tape backings and scraps, wipe the work surface as directed and wash hands if needed.
2 min: Individual design-cycle exit.
Adaptation: New Made by Matt pupil wording and tasks based on the listed uploaded teaching materials. Full lesson preparation, fallback, answers and resource sheets are in the Teacher Guide.
[Sources]
Uploaded Textiles Week 5 teaching and process resources — — DT_Aut1_W5_Textiles_Fabrics_and_Joining.pptx; DT_Aut1_W5_Log_My_Fabric_Lab.docx; DT_Aut1_W5_My_Fabric_Lab_Worksheet.docx. Adapted with optional sensory contact, prepared stitch inspection and fair test evidence; removes claims that one join always wins.
Uploaded Textiles Week 6 design lesson — — DT_Aut1_W6_Textiles_Design_My_Item.pptx. Original new brief, inspiration cards, dimensioned pattern and construction method make the design task self-contained. The uploaded bag/decoration choice is represented by a small card pocket and a flat-decoration alternative.
GROW Autumn scheme of work — Textiles Weeks 5–7 — https://madebymatt.uk/Lessons/_next6/sow/GROW.json — Read reference/_next6/sow/GROW.json: sheet GROW Weekly - Autumn, rows 163, 164, 165. Week 5 explores fabrics/joins; Week 6 designs an item; Week 7 makes/evaluates. Week 7 in this pack is newly authored from that sequence; no Week 7 textile deck was supplied. BUILD adaptations use the shared BUILD/GROW labels in the uploaded Week 5–Week 6 decks, not a claimed independent BUILD SOW verification.
Original classroom pattern and sample data — — All designs, exact dimensions, fictional users and sample join/prototype records were authored for this pack. Data are illustrative, not test certificates. Actual material, adhesive, tool and handling/cure instructions require school approval. No formal ASDAN/AQA attainment or award is promised.
Visual reference and approved brand image: GROW Humanities Week 3 deck supplied by Matt; approved-mark SHA-256 f1095531d88d17f20c7464c62887703321a0872f108d3fb78a4afc0226dac2a7.
[/Sources]