## Slide 1
BUILD SCIENCE
Opening
2 min
Which sample drains most?
Soil: let the water through
1 / 14
Learning intention
Compare how much water passes through different soils in the same time.
A puddle stays on one patch.
Another patch drains sooner.
How can we compare soils fairly?
Notes: Stage allocation: 2 minutes.
Present a familiar school-ground problem without assuming an actual site condition. Today we test samples, not decide the whole grounds design. Pupils can choose equipment or a paper lab.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 2
BUILD SCIENCE
Retrieval
3 min
Find the missing links
Soil: let the water through
2 / 14
1. Name two solid parts of soil.
2. What is a pore?
3. Which is more: 20 mL or 40 mL?
Notes: Stage allocation: 3 minutes.
Retrieve prior soil lesson but provide the answers and a brief recap if this is taught separately. Ask pupils to show the larger number privately.
REVEAL / MODEL ANSWER
1 Mineral and organic material. 2 A space between particles. 3 40 mL.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 3
BUILD SCIENCE
I do
3 min
Follow a connected path
Soil: let the water through
3 / 14
Broad connected paths
Narrow connected paths
A model of pathways, not a rule for every soil.
Water moves through connected pores. Pore size and connections matter. Real soil is more complex.
Notes: Stage allocation: 3 minutes.
Trace the broad blue route. Think aloud: I am looking for a connected route, not counting how brown the soil looks. In real soils, roots, cracks, particle mixtures and compaction affect paths. Do not teach that clay has fewer total pores than sand; tiny pores can hold water while large connected pores let it flow more freely.
DIAGRAM DESCRIPTION
Two simplified pore networks. Broad connected paths permit easier flow than narrow connected paths in this model. Real soil also contains cracks, roots and aggregates; circle sizes are not to scale.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 4
BUILD SCIENCE
I do
2 min
Give each soil the same test
Soil: let the water through
4 / 14
Identical pot + filter
60 mL added
over 10 seconds
Read collected
water at the
same time.
Water
enters
100 cm³ soil
Loose; no tamping
Collection container
Diagram shows collection separately
so all parts are visible.
Same soil volume: 100 cm³. Same water: 60 mL. Read at exactly 2 minutes.
Notes: Stage allocation: 2 minutes.
Explain that the receiver sits directly below the draining pot in the actual setup; the diagram separates the parts for clarity. Demonstrate the method: start timer with first water, pour over 10 seconds, read at 2 minutes. Same pot/filter, loose packing and starting moisture. We compare water collected, a classroom indication of ease of drainage, not an intrinsic permeability coefficient.
DIAGRAM DESCRIPTION
A draining pot holds 100 cubic centimetres of loosely filled soil above a matching filter and support. Sixty millilitres of water is added over ten seconds. A graduated container collects the water for a fixed time.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 5
BUILD SCIENCE
I do
2 min
Read the scale carefully
Soil: let the water through
5 / 14
60 mL
40 mL
20 mL
0 mL
Look at
water level
This level is
30 mL.
Read between marks. Keep the container upright.
Keep the container upright. Look at the water level. Read the volume in mL. What volume is shown?
Notes: Stage allocation: 2 minutes.
Think aloud: the scale goes 0, 20, 40, 60. The level is halfway between 20 and 40, so 30 mL. This is a flat-surface model. With clear water in a narrow cylinder, read the bottom of the curved meniscus at eye level; with cloudy drainage use the visible surface consistently. Choose apparatus with a readable scale.
REVEAL / MODEL ANSWER
30 mL: halfway between 20 and 40 mL.
DIAGRAM DESCRIPTION
A simplified upright measuring cylinder with a level at 30 millilitres. The zero is at the bottom; equal distances represent equal 20 millilitre intervals. Read the surface at eye level.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 6
BUILD SCIENCE
We do
4 min
Repair the unfair test
Soil: let the water through
6 / 14
Choose the useful test cards. Fix any card that changes two things.
Card | Plan
A | All pots: 60 mL; read at 2 min
B | A: 60 mL; B: 100 mL
C | All pots: 100 cm³; loose fill
D | Pack C tightly; leave A and B loose
Constructed planning cards; identical apparatus is assumed
Notes: Stage allocation: 4 minutes.
Work together as a test-design team. Each pupil selects one repair. B would confound water amount with soil; D would confound packing with soil. Same loose fill does not guarantee identical microscopic structure, but controls the action we take.
REVEAL / MODEL ANSWER
Use A and C. Repair B: equal water. Repair D: the same loose preparation.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 7
BUILD SCIENCE
We do
4 min
Read; compare; justify
Soil: let the water through
7 / 14
Compare trial 1. Which sample let most water through? What makes this a fairer comparison?
Soil | Trial 1: mL out | Trial 2: mL out
A | 42 | 40
B | 26 | 28
C | 10 | 12
Constructed sample data • 60 mL in • collect at 2 minutes
Notes: Stage allocation: 4 minutes.
Cover trial 2 briefly if helpful. Invite one learner to read, one compare, one justify. A> B> C in trial 1. Reveal trial 2 and note the same ordering. Constructed values illustrate reasoning; they are not real class results or universal values for named soil types.
REVEAL / MODEL ANSWER
A: 42 mL. It is more than B: 26 and C: 10. Input and time were the same.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 8
BUILD SCIENCE
Hinge
3 min
What can we conclude?
Soil: let the water through
8 / 14
Choose the best claim.
A
A let most water through in this two-minute test.
B
C is the best soil for every plant.
C
A must always drain fastest outdoors.
Notes: Stage allocation: 3 minutes.
All pupils commit first. If they choose B/C, point to the phrase “in this test”. If data comparison is wrong, line up the values 42, 26, 10 on a number line. Proceed to an appropriately supported independent route.
A. A let most water through in this two-minute test.
Correct. A has the largest collected volume under the matched test conditions.
B. C is the best soil for every plant.
This test alone does not measure every plant need or all soil properties.
C. A must always drain fastest outdoors.
Outdoor structure, depth, cracks and starting moisture can change drainage.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 9
BUILD SCIENCE
You do
2 min
Take a role; choose a route
Soil: let the water through
9 / 14
Timer, reader or recorder.
Or work with the paper data.
Use a result to justify your claim.
Notes: Stage allocation: 2 minutes.
Choice is about access and evidence. Practical groups can test one soil and share class results, while individuals complete their chosen page. Paper pupils use both supplied trials. All routes need a compared result and a conclusion.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 10
BUILD SCIENCE
You do
Our method in six actions
Soil: let the water through
10 / 14
Fill; measure; start timer.
Pour; collect; read.
Keep the conditions the same.
Notes: Continue within the time allocated to this stage.
Use identical draining pots and matching filters. Loosely fill each with 100 cm³ of prepared soil, without tamping. Add 60 mL over 10 seconds. Start timing when pouring starts. Collect and read at the stated time. Use fresh equally prepared portions for repeats. Keep soil out of the collection scale. Read at 2 minutes from the start of pouring. For practical pupils, a class trial plus the printed repeat can be compared but never presented as two class trials; label the source of each set.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 11
BUILD SCIENCE
You do
10 min
Make the evidence count
Soil: let the water through
11 / 14
Write the volume with mL.
Compare A, B and C.
Finish: “In this test, __ because __.”
Notes: Stage allocation: 10 minutes.
Circulate during the working time. Use practical readings if valid and record spills/overflow as failed trials needing a repeat; do not replace inconvenient data silently. Pupils using paper data must label them constructed sample data.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 12
BUILD SCIENCE
You do
Check before you claim
Soil: let the water through
12 / 14
Did each test use the same input?
Did we read at the same time?
Does my claim name this test?
Notes: Continue within the time allocated to this stage.
Shares the independent time. Prompt a self-correction rather than adding another worksheet. A conclusion can be spoken and adult-scribed.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 13
BUILD SCIENCE
Review
3 min
Lundy loop: improve our test
Soil: let the water through
13 / 14
Share one result or concern.
Listen for a different observation.
Choose one useful improvement.
What would make our comparison more trustworthy?
Notes: Stage allocation: 3 minutes.
Act on one pupil suggestion by adding it to the class method. State the influence: “We are changing our instruction because you spotted…” If using supplied data only, revise the model protocol, not pretend a real trial occurred.
REVEAL / MODEL ANSWER
For example: matched preparation, an equal pour time, accurate readings or fresh repeated trials.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.

## Slide 14
BUILD SCIENCE
Exit
2 min
Leave with an evidence claim
Soil: let the water through
14 / 14
E1. Which drained most in the sample data?
E2. Name one condition kept the same.
E3. Can this choose the best soil for every plant?
Notes: Stage allocation: 2 minutes.
Record core success when pupil compares a volume and identifies a matched condition. If not secure, reteach with just A and C and concrete number cards before the retention lesson.
REVEAL / MODEL ANSWER
A. For example, 60 mL input or 2 minutes. No: more evidence about plant needs is needed.
LESSON REFERENCES
USDA NRCS: Soil Infiltration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Infiltration.pdf
Checked 8 September 2026. Supports effects of pores, texture, initial moisture and compaction on water movement. Our pot drainage test is a comparative classroom model, not a measurement of field infiltration or intrinsic permeability.
USDA NRCS: Soil Bulk Density, Moisture and Aeration — Guides for Educators
https://www.nrcs.usda.gov/sites/default/files/2022-10/Soil%20Bulk%20Density%20Moisture%20Aeration.pdf
Checked 8 September 2026. Supports pore space, stored water, organic matter and the distinction between water held and water available to plants. Short-time classroom water balance is an estimate and not a field-capacity measurement.